## Slide 1: CCS Technology Status
CMTC Workshop
March 15, 2018
Strategies to Advance Carbon Capture

## Slide 2: Classifying CO2 Sources
Category | % CO2 (vol) | Example
High Pressure | varies | Gas Wells (e.g., Sleipner) Synthesis Gas (e.g., IGCC)
High Purity | 90-100% | Ethanol Plants Oxy-Combustion Exhaust
Dilute | 10-20% | Coal-Fired Power Plants Cement Plants Cracker Exhaust
Very Dilute | 3-7% | Natural Gas Boilers Gas Turbines
Extremely Dilute | 0.04 – 1% | Ambient Air Submarines/ Space Craft

## Slide 3: Capture Technology

## Slide 4: Pros/Cons for Amines
Pros
  Commercially proven
  Closing gap with minimum work
  Scales well
Cons
  Temperamental about impurities
  Requires steam (not plug and play)
  Limits flexibility

## Slide 5: Reseach Focus
Main focus to date has been to reduce the energy penalty
The following are becoming increasingly important:
  Flexibility
  Storage
  Low capital costs

## Slide 6: Market Challenges
Power
  Lowering capacity factors for base load – disadvantages high capital cost systems
  Premium for flexibility
    Load following
    Turndown
    Storage
Industrial
  Lack of steam

## Slide 7: New Capture Process Pathways
Post-combustion Capture
  Adsorption
  Membranes
  Cryogenics
  Fuel Cells
New Power Cycles
  Gasification with pre-combustion
  Oxy-combustion
  Chemical looping

## Slide 8: Gasification
At one point, anointed the future of clean coal and CCS
  High efficiencies
  Criteria pollutant clean-up
  CCS
Issues
  Availability
  High capital costs
Biomass Integrated Gasification (BIG)
  Still prominent in literature
  Tougher than IGCC with coal
    Feeding biomass
    Moisture

## Slide 9: Allam Cycle
Net Power, CB&I, Exelon, Toshiba
50 MWth prototype under construction near Houston
  Broke ground March 9th, 2016
Turbine inlet: 300 bar, Turbine outlet: 30 bar, ~97% recycle

## Slide 10: Cryogenic Carbon Capture
Post-combustion
SES Innovation
  Prof. Larry Baxter
  Brigham Young Univ.
Demonstrated at 1 tpd at coal plants
Features
  No steam required (plug and play)
  Multipollutant capture
  Energy storage

## Slide 11: Geologic Storage

## Slide 12: Geologic Storage Status
Commercial Analogues
  Enhanced Oil Recovery (EOR) – since 1972
  Acid Gas Injection – since 1989
  Natural Gas Storage – since 1915
Commercial Operations: 6 projects at megaton/yr scale
Subsurface Uncertainty
  Capacity
  Long-term Integrity
  Induced Siesmicity
Other Issues
  Regulatory Framework
  Long-term Liability
  Public Acceptance
Passive vs. Engineered Systems

## Slide 13: Utilization

## Slide 14: Utilization
Use | Market Size | Permanence | Life-Cycle Energy | Comments
EOR | 0 | + | 0 | Stepping Stone
Mineralization | + | + | Theory: + Reality: - | Opportunities in Cement
Chemicals, etc. | - | - | - | Niche Applications
Fuels | + | - | - | Costly

## Slide 15: Negative Emissions

## Slide 16: CO2 Removal Options
BECCS: Bioenergy with carbon capture and storage
DAC: Direct air capture of CO2 from ambient air by engineered chemical reactions
EW: Enhanced weathering of minerals, where natural weathering to remove CO2 from the atmosphere is accelerated and the products stored in soils, or buried in land or deep ocean
AR: Afforestation and reforestation to fix atmospheric carbon in biomass and soils
Ocean: Manipulation of carbon uptake by the ocean, either biologically (that is, by fertilizing nutrient-limited areas) or chemically (that is, by enhancing alkalinity)
Agriculture: Altered agricultural practices, such as increased carbon storage in soils
Biochar: Converting biomass to recalcitrant biochar, for use as a soil amendment.
From Smith, et al., “Biophysical and economic limits to negative CO2 emissions”, Nature Climate Change, 6, January (2016).

## Slide 17: Negative Emissions
BECCS
  Require carbon prices ~$100/tCO2
    Avoids paying the carbon price
    Receives carbon credits for negative emissions
  Major barrier – finding carbon neutral biomass
DAC
  Require carbon prices ~$1000/tCO2 or carbon-free power that is too cheap to meter

## Slide 18: Role of Negative Emissions
Lower atmospheric CO2 levels
  Purpose: Meet an [arbitrary] stabilization target
  Scale: 10s Gt CO2/yr
  Cost: > > today’s mitigation costs
Offsets
  Purpose: Offset emissions that are very expensive to mitigate
  Scale: Gts CO2/yr
  Cost: < marginal mitigation cost at any time

## Slide 19: Scenarios

## Slide 20: Global Results to 2100
Base
Cheaper Renewables
Cheap Nuclear
Cheap CCS

## Slide 21: Major Regional Results to 2100
USA
EUR
India
China

## Slide 22: Closing Thoughts
Carbon Dioxide Capture and Storage (CCS) is technically viable today and has significant scope for improvement.
While there is room to improve costs, it will always be cheaper to emit CO2 to atmosphere than capture. Therefore, policy is required to make CCS economically viable.
A low carbon energy system will have significant differences from today’s energy systems. We need to develop innovative CCS technology that fits with tomorrow’s systems.
Utilization and negative emissions are hot topics in CCS today. We may need to pump the brakes a bit.

## Slide 23: Contact Information
Howard Herzog
Senior Research Engineer
Massachusetts Institute of Technology (MIT)
Energy Initiative
Room E19-370L
Cambridge, MA 02139
Phone: 617-253-0688
E-mail: hjherzog@mit.edu
Web Site: sequestration.mit.edu